## Slide 1: A Mathematical Modelling Study of the Effects of Air Expansion in the Brain on the Intracranial Pressure
Viruj, Bala Soupramanien
Supervisor: Dr. Ooi Ean Hin
Moderator: Dr. Chiew Yeong Shiong

## Slide 2: Contents
Project objectives
Background
Previous studies
Methodology
Results
Conclusion

## Slide 3: Project Objectives
Mathematically model the intracranial system to include intracranial air
Investigate the effects of altitude change on the system
Investigate the effects of temperature change on the system

## Slide 4: Background

## Slide 5: Pneumocephalus
A collection of intracranial gas
Traumatic pneumocephalus:
  Severe head injuries
Nontraumatic pneumocephalus:
  Extracranial infections
  Performing Valsalva manoeuvres
  Barotrauma
  Post-craniotomy

## Slide 6: Dangers of Pneumocephalus
< 1500 mm Hg (200 kPa); air ideal gas
Gas trapped in body cavities will expand
  Decrease in pressure (Boyle-Mariotte’s law)
  Increase in temperature (Charles’ law)
Rate of intracranial air accumulation continuously increase
Can cause mass effect on brain
Intracranial pressure rises

## Slide 7: Intracranial Pressure
Pressure the cranium exerts on intracranial compartments
Monroe-Kellie hypothesis:
  Cranium consists of brain parenchyma, cerebral blood and cerebrospinal fluid
  Various mechanisms to maintain stable intracranial pressure
Cerebral autoregulation:
  Shifting cerebrospinal fluid into spinal compartment
  Increased absorption rate of cerebrospinal fluid
  Cerebral blood displacement out of the cranium

## Slide 8: Previous Studies
Modelling of intracranial system
  Marmarou et al. (1978)
  Meier et al. (1999)
  Lakin et al. (2003)
  Eklund et al. (2007)
Modelling of intracranial system including intracranial air
  Anderson et al. (2003)
Mathematical studies non-invasive

## Slide 9: Methodology

## Slide 10: Model Schematics
IIA
If
Itot
Ir
Ia
C(PIC)
R
Pd
PIC
Analogous electrical system describing the hydrodynamic system
Anderson, N., Grip, H., Lindvall, P., Koskinen, L., Brandstrom, H., Malam, J., & Eklund, A. (2003). Air Transport of Patients with Intracranial Air: Computer Model of Pressure Effects. Aviation, Space And Environmental Medicine, Vol. 74(2), 138-144.

## Slide 11: Anderson et al. (2003) Model
Intracranial air pressure varies with:
  Atmospheric pressure (75-100 kPa)
  Intracranial pressure (1-3 kPa)
Intracranial air pressure Atmospheric pressure
Linear approximation

## Slide 12: Assumptions
Hydrodynamic equilibrium between pressure and flow
Re-absorption of air rate negligible
Fluid accumulation from tissue swelling negligible
Rapid cabin decompression not considered
  Only cabin compression
Compared to inputs

## Slide 13: Mathematical Formulation of System
For changing ambient pressure – Boyle-Mariotte’s law:
For changing ambient temperature – Charles’ law
  =

## Slide 14: Parameter Selection Effects of Altitude Change on System
Parameter | Value
PICr | 10 and 20 mm Hg
PVI | 12.6 ml
R | 16.1 mm Hg ml-1 min-1
VIA0 | 10, 20 and 30 ml
dH/dt | 250, 500 and 1000 ft min-1
X | 2288, 2824 and 3641
Y | 141.49, 223.04 and 375.23
Z | 0.0015, 0.0026 and 0.0042
Parameter values for model
Linear, logarithmic and exponential functions of altitude with time

## Slide 15: Parameter Selection Effects of Temperature Change on System
 | 18 | 21 | 24
10 | 3.54 | 2.97 | 2.45
20 | 2.32 | 1.95 | 1.58
30 | 1.25 | 1.05 | 0.85
VIA0 (ml)
Ti (°C)
Time rate of temperature change for all initial volumes and temperature
Fong, K. (2010). Surgeons use cold to suspend life. [online] BBC News. Available at: https://www.bbc.com/news/health-11389464.

## Slide 16: Parameter Selection Effects of Temperature Change on System
(a) 10 ml
(b) 20 ml
(c) 30 ml
Change in body temperature with time for all initial volumes and temperature
(a) 10 ml
(b) 20 ml
(c) 30 ml

## Slide 17: Results
Effects of Changing Ambient Pressure

## Slide 18: Constant Ascension Rates
(a)
(b)
Change in intracranial air volume during ascent at 500 ft min-1, simulated for three initial volumes
Change in intracranial pressure during ascent at 500 ft min-1 simulated for three initial volumes for (a) 10 mm Hg and (b) 20 mm Hg resting pressure

## Slide 19: Exponential Ascension
(a)
(b)
Change in intracranial air volume during exponential ascent, simulated for three initial volumes
Change in intracranial pressure during exponential ascent, simulated for three initial volumes for (a) 10 mm Hg and (b) 20 mm Hg resting pressure

## Slide 20: Logarithmic Ascension
(a)
(b)
Change in intracranial air volume during logarithmic ascent, simulated for three initial volumes
Change in intracranial pressure during logarithmic ascent, simulated for three initial volumes for (a) 10 mm Hg and (b) 20 mm Hg resting pressure

## Slide 21: Results
Effects of Changing Ambient Temperature

## Slide 22: Change in Intracranial Air Volume
(a)
(b)
(c)
Change in intracranial air volume with change in temperature simulated with three initial volumes and (a) 18 °C, (b) 21 °C and (c) 24 °C, initial temperatures

## Slide 23: Change in Intracranial Pressure
(a)
(b)
(c)
Change in intracranial pressure with change in temperature simulated with three initial volumes, 10 mm Hg resting pressure and (a) 18 °C, (b) 21 °C and (c) 24 °C, initial temperatures

## Slide 24: Change in Intracranial Pressure
(a)
(b)
(c)
Change in intracranial pressure with change in temperature simulated with three initial volumes, 20 mm Hg resting pressure and (a) 18 °C, (b) 21 °C and (c) 24 °C, initial temperatures

## Slide 25: Conclusion
Revision of model proposed by Anderson et al. (2003)
Intracranial pressure depends on ascension rates and rate of temperature change
Intracranial pressure can reach high levels
  High initial intracranial air volume
  High ascension rate
  Low initial temperature

## Slide 26: References
Anderson, N., Grip, H., Lindvall, P., Koskinen, L., Brandstrom, H., Malam, J., & Eklund, A. (2003). Air Transport of Patients with Intracranial Air: Computer Model of Pressure Effects. Aviation, Space And Environmental Medicine, Vol. 74(2), 138-144.
Eklund, A., Smielewski, P., Chambers, I., Alperin, N., Malm, J., Czosnyka, M., & Marmarou, A. (2007). Assessment of cerebrospinal fluid outflow resistance. Medical & Biological Engineering & Computing, 45(8), 719-735.
Fong, K. (2010). Surgeons use cold to suspend life. [online] BBC News. Available at: https://www.bbc.com/news/health-11389464.
Lakin, W.D., Stevens, S.A., Tranmer, B.I. and Penar, P.L., 2003. A whole-body mathematical model for intracranial pressure dynamics. Journal of mathematical biology, 46(4), pp.347-383.
Marmarou, A., Shulman, K., & Rosende, R. (1978). A nonlinear analysis of the cerebrospinal fluid system and intracranial pressure dynamics. Journal Of Neurosurgery, 48(3), 332-344.
Meier, U., Zeilinger, F.S. and Kintzel, D., 1999. Diagnostic in normal pressure hydrocephalus: A mathematical model for determination of the ICP-dependent resistance and compliance. Acta neurochirurgica, 141(9), pp.941-948.
Peterson, E., Kent, B., & Cone, W. (1944). Intracranial pressure in the human subject at altitude. Archives of Neurology and Psychiatry, 52(6), 520.

## Slide 27: Thank You